## Slide 1
KONGU ENGINEERING COLLEGE
Computer Science & Engineering
Intelligent Irrigation Controller
Sweta T (24CSR316)
Tharun R (24CSR323)
Anandhakrishna J (24ECR013)
Subiraj B (24ECR0__)
Guided by
Dr. K. Dinesh
(Associate Professor)

## Slide 2
KONGU ENGINEERING COLLEGE
Problem Statement
Irrigation is still decided by eye, causing wasted water (over-irrigation) or crop stress (under-irrigation). Soil moisture alone is reactive: it ignores incoming rain and how fast the crop loses water. The proposed Intelligent Irrigation Controller:
Predicts irrigation need from soil moisture, real weather data and evapotranspiration (ET) computed with the FAO-56 Penman-Monteith equation
Automates the valve from an ESP32 edge node reading a 7-in-1 RS485 NPK probe, closing the loop locally with a fail-safe rule
Gives the operator a dashboard with schedules, water-stress alerts and per-zone nutrient guidance
Uses a two-stage gradient-boosted model: decide whether to irrigate, then how deep, with a cost-weighted operating point
Secondary outputs: crop disease-risk, NPK fertiliser dose and yield estimates from the same reading
SDG 2 (Zero Hunger), SDG 6 (Clean Water and Sanitation), SDG 12 (Responsible Consumption and Production)

## Slide 3
KONGU ENGINEERING COLLEGE
Research Gap
Existing Challenges
Most published systems are reactive: no forecast, no evapotranspiration term
Noisy, intermittent soil readings amplify into large irrigation errors on deep root zones
Fuzzy or rule-only schedulers need site-specific tuning and cannot transfer between districts
No public dataset pairs NPK soil telemetry with confirmed crop disease, so disease models are hard to validate honestly
Edge-only or cloud-only designs trade accuracy against latency and uptime
Proposed Solution
Soil moisture plus real satellite meteorology plus a validated FAO-56 ET0
Two-stage gradient boosting: irrigation decision, then irrigation depth in mm
Forward soil water balance simulation over real weather, plus probe-noise injection and causal temporal smoothing
Automated valve control with a live operator dashboard
Disease risk, NPK dose and yield as add-on insights from the same reading

## Slide 4
KONGU ENGINEERING COLLEGE
Objectives and SDG Relevance
Objectives
Forecast irrigation requirement from real soil moisture, NASA POWER meteorology and FAO-56 evapotranspiration
Automate valve control from an ESP32 edge node with a 7-in-1 RS485 NPK probe and a latching solenoid, fail-safe on loss of link
Deliver an operator dashboard with zone schedules, water-stress alerts and nutrient guidance
Report disease risk, fertiliser dose and yield as additional insights, with an explicit statement of what each figure does and does not mean
SDG Relevance
SDG 2 – Zero Hunger: improve productivity and food security.
SDG 6 – Clean Water and Sanitation: raise water-use efficiency through predictive irrigation.
SDG 12 – Responsible Consumption and Production: conserve water and reduce agricultural losses.

## Slide 5
KONGU ENGINEERING COLLEGE
Proposed Methodology
1 Data Collection
10 years of daily meteorology from NASA POWER (12 stations, 43,836 days) plus 7-in-1 NPK soil telemetry
2 Feature Engineering
FAO-56 ET0, soil water deficit, wetness ratio, crop stress index, causal 3- and 7-day trend features
3 Stress Synthesis
Forward soil water balance integrated over the real weather record; hysteresis irrigation rule; physically derived targets
4 Irrigation Planning
Applied depth in mm, pump runtime, deficit and excess risk levels per zone
5 Data Augmentation
Probe measurement-noise injection, per-zone nutrient drawdown, rainfall gap handling
6 Model Training
8 models: gradient-boosted classifiers and regressors; two-stage irrigate/depth design; cost-tuned decision threshold
7 Evaluation
Stratified grouped split on unseen field series, plus a fully held-out station; macro F1, MAE, R², permutation importance, latency
Output
Depth and volume, valve runtime, soil-water trend, stress and nutrient alerts, disease risk, confidence

## Slide 6
KONGU ENGINEERING COLLEGE
Model Training Approach
Features Used
Air temperature, relative humidity, wind speed
Soil moisture, plus 3- and 7-day mean and trend
Soil pH and electrical conductivity
Nitrogen, phosphorus, potassium (mg/kg)
Light intensity (lux) and rainfall
Crop stress index, derived from the above
Configured: crop, soil class, root depth, field capacity, field area; from weather: ET0 and Kc
Models: HistGradientBoosting
Stage 1 classifier: irrigate or hold
Stage 2 regressor: depth in mm, on irrigation events
max_iter 220/260, max_depth 8, lr 0.07-0.09
min_samples_leaf 30-40, L2 0.6-1.0
Threshold tuned 3:1 toward missed irrigation
Disease F1 0.908, depth MAE 1.05 mm (R2 0.963), <0.01 ms

## Slide 7
KONGU ENGINEERING COLLEGE
Workflow Diagram
7-in-1 RS485 NPK probe + air temperature, humidity and lux
→
NASA POWER daily meteorology, 12 stations, 2015-2024
→
FAO-56 ET0, soil water deficit, wetness ratio, stress index, 3- and 7-day trend features
→
Forward soil water balance simulation over real weather
Two-stage gradient boosting, grouped and unseen-station evaluation
→
Irrigation decision + depth in mm + valve runtime
→
ESP32 -> relay -> latching solenoid valve, fail-safe on link loss
→
FastAPI + WebSocket -> React dashboard: schedules, alerts, what-if
↓
Feedback loop: the probe re-measures after the valve closes, and the next cycle starts from the new state. Secondary branch off the model: disease risk, NPK dose and yield.

## Slide 8
KONGU ENGINEERING COLLEGE
Reference
[1] R. G. Allen, L. S. Pereira, D. Raes and M. Smith, "Crop evapotranspiration: guidelines for computing crop water requirements," FAO Irrigation and Drainage Paper 56, Rome, 1998. (Source of the ET0, soil water balance and Kc equations.)
[2] NASA Prediction of Worldwide Energy Resources (POWER) Project, daily agroclimatology point API, 12 stations, 2015-2024. https://power.larc.nasa.gov/docs/services/api/temporal/daily
[3] G. Saha et al., "Smart IoT-driven precision agriculture: Land mapping, crop prediction, and irrigation system," PLOS ONE, vol. 20, no. 3, e0319268, Mar. 2025.
[4] F. Z. Bassine et al., "Recent applications of machine learning, remote sensing, and IoT approaches in yield prediction: a critical review," arXiv:2306.04566, Jun. 2023.
[5] V. H. U. Eze et al., "Integrating IoT sensors and machine learning for sustainable precision agroecology," Discover Agriculture, vol. 3, Art. 83, May 2025.